Bluetooth Connectivity

1. Turn on both units.

2. On both units, navigate, on the home page, to the Bluetooth symbol, and select it by pressing the orange button.

3. On both units, make sure the Bluetooth is turned on and visible.

Home Page ( Bluetooth ( On/Off

Home Page ( Bluetooth ( Visibility ( Visible

4. On the unit that is sending the message, select ‘Search’ on the Bluetooth menu. Wait while the unit searches. When the results are displayed, select the ‘NXT’ symbol and connect it to the other unit.

Home Page ( Bluetooth ( Search ( NXT ( Connect ( Then choose whatever connection is specified in your program.

If you selected the right NXT (since there is no way to differentiate between multiple NXTs that have Bluetooth enabled), then both units will prompt you to enter a passkey. The default passkey is set to 1234, and should be sufficient. If, however, you have not connected to the right NXT, the passkey will not appear on both units, and you need to repeat the search process and try to connect to a different NXT.

5. After you have established a connection, it will remain until you shut the NXT off, or until it randomly looses connection. The following steps will explain how to easily connect two NXTs that have been connected in the past.

6. Turn on the NXT, and from the main menu, navigate to the Bluetooth menu.

7. On the Bluetooth menu, select ‘Contacts’. Then choose whichever NXT you would like to connect to, and whichever connection specified in you program.

Home Page ( Bluetooth ( My Contacts ( Choose the NXT Needed ( Choose the Connection Specified in Program.